## Slide 1: Eve Kit Software Installation
Michael Clayton
December 23, 2024

## Slide 2
TSP Information
Logistic Information
Procedure
Appendix
For INFORMATION
For DECISION
For DIRECTION
X
X
X
Contents
X

## Slide 3
TSP-J-5014
N/A
N/A
Eve Kit Software Installation
N/A
N/A
No
Yes
No
N/A
N
N/A
Rafael Guillen
12/23/2024
N/A
Michael Clayton
Chris Lewandowski
Converted to the NEW 5080 PPT format
240
4.0
0.5
N/A
N/A

## Slide 4
Ryan Bednar
8/28/2024
Michael Clayton
8/28/2024

## Slide 5
Technician/s Needed to Perform Test: 1
Location where Test will/can be performed.
  Lab/Room 1 - # of Days Required
Hardware Needed
  Eve kit
  Battery box
  External monitor with HDMI and Power
  Keyboard
  USB Storage Device
Computer interface needed
  CANoe
  CANape
  Vector Hardware Configurator
  Vector Hardware Manager
  Google Chrome

## Slide 6
Basic Setup
Step | P R O C E D U R E
1 | Contact ADAS team to acquire all the necessary items needed to complete the software installation
2 | Download “New Eve Software” This can be found on Box https://nissan-usa.app.box.com/folder/287207437413?s=onrog3vgklgdjttm8c3rjm1cdx400h1e If you are unable to download the folder, a team member will be able to assist (Photo # 1)
60
1

## Slide 7
5
Basic Setup
Step | P R O C E D U R E
3 | Plug in battery Anderson connector to Anderson connector on the lower right of the Eve Kit. (Photo # 2) Plug in monitor to HDMI slot on patch panel and any monitor power to USB slot. (Photo # 4) Plug in keyboard and storage device into USB slot on patch panel. (Photo # 4)
4 | Turn battery on. (Photo # 3) Turn Main power rocker on and wait 2-3 seconds. (Photo # 4) Turn PC power rocker on. (Photo # 4)
2
3
4

## Slide 8
1
Basic Setup
Step | P R O C E D U R E
5 | Search for “File Explorer” right click and choose “Pin to Taskbar” (Photo # 5)
6 | Search for Settings Once in the Settings Window select “Time and Language” (Photo # 6)
5
6

## Slide 9
1
Basic Setup
Step | P R O C E D U R E
7 | In the Date & Time Tab, change time Zone to Eastern Time (Photo # 7)
8 | In the Language tab, change Windows, Apps, Regional Format, Keyboard, and Speech to English (Photo # 8) Changes can be made by clicking on the icon and adjusting language in pull down window
7
8

## Slide 10
Update Drive Letters and Rename
Same drive letter setup across ADT FH/SAC/AZ
Change Drive Letters
Previous D Drive -> Change to E Drive
  Rename to “Setup”
  This drive should have ~100Gb of space
Previous E Drive -> Change to D Drive
  Rename to “Data”
  Ensure this is the drive with 4+ TB of space
Andre

## Slide 11
Change Axis Quad IP Addresses
Same IP setup across ADT FH/SAC/AZ
Axis Quad IP Address Change
Manually change each Axis Quad IP Address in Axis software
  Axis Quad 1 -> 195.0.100.1
  Axis Quad 2 -> 195.0.100.2
  Axis Quad 3 -> 195.0.100.3
  Default Router = 195.0.100.10 (Same for all Axis)
Andre

## Slide 12
Change Brick PC Port IP Settings
Same IP setup across ADT FH/SAC/AZ
Brick PC Port IP Settings for Axis Cams
Place batch file in Brick Settings Folder
  This PC -> Downloads -> Brick Settings
  BrickPC_ip_config_New_Axis.bat
Confirm Network names are matching image on right
Right click batch file -> Run As Administrator
Assignments are the following, also shown below
  1G #1 -> 195.0.100.11
  1G #2 -> 195.0.100.12
  1G #3 -> 195.0.100.13
  1G #4 -> Same as Previous (192.168.4.1)
  10G #1 -> Same As Previous (192.168.10.10)
Andre
Batch File Placement
Required Network Naming

## Slide 13
10
Software download
Step | P R O C E D U R E
17 | Transfer the “New Eve Software” from your storage device to the Downloads folder on the Eve Kit.
18 | Open the BlfReader folder and double click on BlfReader.exe file, and it will begin downloading. (Photo # 17)
17

## Slide 14
9
Software download
Step | P R O C E D U R E
19 | Repeat step 18 for Powershell-7.1.3-win-x64.msi LibreOffice_7.0.4_Win_x64.mis vlc-3.0.17.4-win64.exe ffmpeg.exe ChromeStandaloneSetup64.exe Gpst1_7 (1).exe FastCopy351_Installer64.exe 7z1900-x64.exe (Photo # 18)
18

## Slide 15
5
Software download
Step | P R O C E D U R E
20 | Unzip and download the CANape21.0 File. Double click Setup.exe to begin install
21 | Install to C:\Program Files\Vector CANape21.0 (Photo # 19) Select the Fully Featured or Test Version (Photo # 20) Note the Eve Kit may restart a couple times during install
21
19
20

## Slide 16
1
Software download
Step | P R O C E D U R E
22 | Vector_Driver_Setup_080824 > Vector_Driver_Setup_24_20_2 > Drivers Double click on setup.exe to download the vector tools
23 | Check the boxes to install the following drivers VN1530/VN1531 VN1610/VN1611/VN1630/VN1640 VN1670 VN5650 Vector Time Sync Service GNSS (Photo # 21)
21

## Slide 17
1
Vector License Client
Step | P R O C E D U R E
24 | Work with Andre Apostol, Ryan Bednar, or Michael Clayton to install Vector License to Eve Kit (Photo # 22)
22

## Slide 18
Add to Vector Hardware
Add CAN21 for OxFord Setup
Open Vector Hardware Configuration
Right click CANape -> Application Channel Usage
Ensure all are 0 except the following:
  CAN = 22
  LIN = 5
  GNSS = 1
Andre

## Slide 19
Add CAN21 to Vector Hardware
Assign CAN18 and CAN21
Verify CAN and LIN
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN Channels are accurate
GNSS -> vGNSS Channel 1
Verify Vector Hardware looks exactly the same as image on the right
Andre

## Slide 20
Upgrade to latest drivers
For GPS as Vector Hardware Device
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN2 is VN1670 CH 5
Do not update Vector Platform Manager?
Andre
Confirm latest drivers work

## Slide 21
Upgrade to latest version of CANape 21
CANape 21 SP 6
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN2 is VN1670 CH 5
Do not update Vector Platform Manager?
Andre
Confirm latest CANape 21 version works

## Slide 22
1
Powershell
Step | P R O C E D U R E
38 | Open File Explore folder on task bar
39 | This PC > Windows(C:) > System32 > WindowsPowerShell > v1.0 Scroll down to Powershell.exe, right click and Run and Administrator (Photo # 31)
40 | In the command window (Photo # 32) (1) Type $PSVersionTable *enter* Ensure “PSVersion” = 5.1 (2) Type set-executionpolicy remotesigned *enter* type “A” = Yes to All
31
32
1
2

## Slide 23
2
Axis Hardware
Step | P R O C E D U R E
41 | Unplug the green power connector from the second Axis Encoder (Photo # 33)
Encoder #1
Encoder #2
Power connector
33

## Slide 24
5
Axis Hardware
Step | P R O C E D U R E
42 | Right click on the network icon in the bottom right to go to network settings (1) . Once in network settings, click on “Change adapter options” (2) (Photo # 34)
43 | Right click on the “1G 1” network and go down to properties. (Photo # 35)
34
35
1
2

## Slide 25
1
Axis Hardware
Step | P R O C E D U R E
44 | Click on “Internet Protocol Version 4 (TCP/IPv4)” then click properties (Photo # 36)
45 | Change the IP Address to 192.168.0.10 and click OK (Photo # 37)
36
37

## Slide 26
1
Axis Hardware
Step | P R O C E D U R E
46 | Go to google chrome and type in 192.168.0.90 in the search bar, This will take you to the Axis log in page. For Username: root For Password: root You will then be sent back to the sign in page (Photo # 38)
38
root

## Slide 27
5
Axis Hardware
Step | P R O C E D U R E
47 | Click the yellow Change (1) button on the right side to change the video display settings. (Photo # 39)
48 | Change all video settings to 1280x720 @50/60 fps Click Save and restart. This will prompt the Axis Encoder to restart (Photo # 40)
39
40
1

## Slide 28
1
Axis Hardware
Step | P R O C E D U R E
49 | Under Systems tab, go to Users and Allow Anonymous Viewing (Photo # 41)
50 | Under Systems tab, go to Network, Uncheck Assign IPv4 Automatically (1) Change the IP Address to 192.168.1.95 and click Save. (Photo # 42)
41
42
1

## Slide 29
1
Axis Hardware
Step | P R O C E D U R E
51 | Go back to the network adapters for 1G 1, click on “Internet Protocol Version 4 (TCP/IPv4)” then click properties (Photo # 43)
52 | Change the IP Address back to 192.168.1.1 and click OK (Photo # 44)
43
44

## Slide 30
5
Axis Hardware
Step | P R O C E D U R E
53 | Unplug the green power connector from the first Axis Encoder and plug power connector in for second Axis Encoder (Photo # 45)
Encoder #1
Encoder #2
Power connector
45

## Slide 31
20
Axis Hardware
Step | P R O C E D U R E
54 | Repeat steps 36-45 but for Network 1G 2. - When you reach step 43 the IP address will be 192.168.2.96 - When you reach step 45 the IP address will be 192.168.2.1
55 | If there is a 3rd Axis Encoder; Repeat steps 36-45 but for Network 1G 3. - When you reach step 43 the IP address will be 192.168.3.97 - When you reach step 45 the IP address will be 192.168.3.1
End of Test | 

## Slide 32
Eve Kit AZ Compatibility
Additional Hardware and Software Eve kit changes
Key Updates for Compatibility
Change Axis Quad IP Addresses
Run batch file to update Brick PC IP Addresses
Update Drive Letters and Rename
Add CAN21 to Vector Hardware for OxFord pluggin
Label CAN18/CAN21 spot on Eve Kit\
Update Vector Drivers to latest (25_10_0)
Update to CANape 21 SP 6 (Final upgrade for CANape 21)
Upgrades for Wifi Data Upload
Remove main USB slot, plug in and mount Wifi 6 Adapter
Update patch panel for one less USB (ensure no confusion or no empty ports)
Setup Synology Drive Client for wifi data upload to NAS
Andre

## Slide 33
Eve Kit Hardware Detail
Individual hardware components contained in the Eve kit
Main Eve Kit Components
VP7470 – Brick PC with 32 Gb RAM
VN1670 – 10 CAN, 5 LIN
VN5650 – 6 Ethernet, 2 CAN
VN1530 – 6 CAN
Axis F44 (x3) – Up to 4 Axis Cameras
ITS1_FD necessary for online tuning
VP7470 – Brick PC
VN1670
VN5650
F44 Axis Encoder

## Slide 34
Eve Kit Hardware Setup
Dedicated hardware CAN assignments for consistency and reliability
Same setup across ADT FH/SAC/AZ
Hardware Setup
Plug in specific CAN device to dedicated port on Eve Kit
  ITS1_FD -> CAN1, ITS2_FD -> CAN2, etc
Beneficial to ensure correct database files, recorded signals, and baud rates
Same hardware and patch panel layout across all 23 Eve Systems
  Exception, old axis cameras (no risk to new configurations)
Andre
CAN 1 - 16
CAN 17 - 18, LIN 1 - 2
ETH 1 - 3
Axis CAM5, CAM6

## Slide 35
Wifi Adapter Addition
Mount Wifi Adapter to Eve Kit
Plug into Brick PC
Mount Wifi Adapter to Eve Kit
Plug USB into Brick PC port 1
Remove patch panel slot for empty USB
  Shift HDMI port left 1
Andre
Need to put picture of official mounting location

## Slide 36
Wifi Data Upload Setup
Activate Wifi on Brick PC
Open file explorer
Choose CD drive Wifi 6 USB
Choose Driver Folder -> Setup.exe
Installation will begin!
  Wait to finish
  Will close automatically when complete
Andre

## Slide 37
Wifi Data Upload Setup
Connect to Orbi Router
After Wifi 6 installation is finished, window will close
Network connections will now have wifi option
Open wifi settings and find ORBI38 router
Choose connect automatically
Password = windylake010
Ensure connected successfully! (No internet, secured)
Andre

## Slide 38
Wifi Data Upload Setup
Install Synology Drive Client Software
Install Synology Client Software
  Software provided by Andre
Click through setup -> very simple
Andre

## Slide 39
Wifi Data Upload Setup
Setup Synology Drive Client
Open Synology Drive Client
Connect to NAS
  Synology NAS = 195.0.100.101, click search
  Choose ADT_DataCenter
  Username = ADT_EveUploader
  Password = PR0P!L0T
  Keep checked “Enable SSL”
  Click Next
Choose proceed anyway
Andre

## Slide 40
Wifi Data Upload Setup
Setup Synology Drive Client
Choose sync task -> click next
View original folder, edit paths on the next slide
Click change to edit folder to sync from NAS
Andre

## Slide 41
Wifi Data Upload Setup
Setup Synology Drive Client
Folder to sync from your NAS (195.0.100.101)
  Expand team folder
  Select CANape_Data
  Click OK
Folder location on your computer
  Expand D Drive
  Select only CANape_Data
  Uncheck create an empty “SynologyDrive” folder
  Click OK
Andre
Folder from NAS
Folder location on computer

## Slide 42
Wifi Data Upload Setup
Setup Synology Drive Client
Initial folder paths should look exactly like the image on the right
But wait not finished!
Click advanced
Under Folder
  Ensure CANape_Data is selected
  Every folder below should be auto selected, no need to change
Change to sync mode tab
Andre

## Slide 43
Wifi Data Upload Setup
Setup Synology Drive Client
Sync mode tab
  Check Upload data to Synology Drive Server Only
  Keep checked “locally deleted files”
  Keep checked “enable advanced consistency check
Ensure settings match the image on the right -> Click Apply!
Andre

## Slide 44
Wifi Data Upload Setup
Setup Synology Drive Client
Ensure file paths are still the same
Enable on demand sync checkbox will be removed automatically -> this is OK
Click done!
Andre

## Slide 45
Wifi Data Upload Setup
Setup Synology Drive Client
Click through everything (Next x4)
Ensure the sync task matches the settings on the right
  D:\CANape_Data
  One-way upload
Andre

## Slide 46
Wifi Data Upload Setup
See tasks when data starts to sync
Go to taskbar settings (right click on taskbar -> taskbar settings)
Scroll down -> Select which icons appear on the taskbar
Find Synology Drive Client -> Switch to ON
Andre

## Slide 47
Wifi Data Upload Setup
See tasks when data starts to sync
Go to D drive folder
Verify syncing status shows blue icon
  Syncing in progress
Green checkmark will show when that folder sync is complete
Andre
Sync in Progress
Sync Complete

## Slide 48
APPENDIX

## Slide 49
CANape Configuration - Setup
Setup page implemented from AZ configuration
Dedicated CAN assignments from hardware to match CANape software
New Setup page
Input Vehicle Project and Number
Select AD Mode -> Supports data driven tuning
Hardware Match
Check CAN boxes based on connected hardware
Selectable dropdown options for Ethernet channels based on Radar, Camera, and HD map type
Check Axis boxes based on external camera setup
Select commit to automatically enable/disable CANape networks in the Device Configuration
  Status of background network displayed with colored LED
  Axis camera views are live output
That’s it!
Andre

## Slide 50
CANape Configuration – Setup Online Tuning
Additional Steps for Online Tuning Configuration
Online Tuning Additional Setup
Navigate to Device Configuration
Expand Online_Tuning under CAN1
Select database -> Replace A2L file to online tune new vehicle
  Different A2L and PDX files for different vehicles
  Check page switching
Andre
Return to LKA1 Page
Ignition or engine on
Click online
Current LKA parameters will be retrieved from the ADAS module software

## Slide 51
CANape Configuration – Confirmation Drive
Take vehicle for data confirmation drive
Ensure green heartbeats and confirm active GPS triggers
Confirmation Drive
Start recording and drive test vehicle to M5 and back to office
  Test of active GPS triggers
  Test blue mode capable for AD2 vehicle
Ensure green heartbeats for successful signal recording
Ensure online tuning is working by verifying parameter changes are successful
Andre
External Comment Box
Executable built with C# to bypass CANape limitations
Allow for multiple comment boxes open at once
Ensures GPS triggers still successfully cut in the background
Turn comments on and off with convenient switch

## Slide 52
CANape Configuration – Automatic Data Cutting
Trigger 1 minute cutout files based on GPS location
New Trigger List Layout
GPS Trigger Output to Trigger List
Automatic cutting of data when driving through key scenes
Data comparing two runs at the same location can be overlaid and plotted easily
New trigger list structure for data review compatibility
New Trigger List
Free comment for individual trigger
GPS Trigger Scene Name
Trigger folder for individual run data

## Slide 53
CANape Configuration – Check Data
Output automatic data check report to confirm reliable data
Output Data Check Report
Return to office, stop recording, allow post processing
  Matlab conversion, automatic data transfer to SSD
Navigate to setup page, select Check Data box
  Check remaining E Drive space
  Script will automatically loop through each folder created from the various recorders
    Recorders 1, 2, 3 and Full
  Verify output file exists and is an appropriate file size (MF4, BLF, AVI, Trigger List CSV, KML)
  Check for important signals in individual MF4 files
    Yaw Rate, Steering Angle etc and ensure numerical output
  Confirm AXIS Camera videos files
  Confirm external SSD is recognized and fast copy is working
See result column to determine success or fail of individual tests
Andre

## Slide 54
CANape Configuration Setup - Additional
Full run MAT conversion to support data driven tuning
Continuous monitoring during driving to ensure no data errors
Full Run MAT Convert
Supports data driven tuning to make vehicle models
Automatic CANape function to convert additional data
Continue to add scripts and features that support users automatically for reliable data collection
  Avoid manual processing and sorting
Continuous Monitoring
Continuous checking of critical recording issues
  Example E drive space
  Pop up will show continuously until recording is stopped
Continue to add to this function to ensure no data loss during recording
Andre

## Slide 55
Data Organization
The Data Center Folder Structure Layout on SSD
CANape Data Organization Overview
The Data Center (CANape Data)
Automatic copy of CANape Data to SSD
Organization by Vehicle Project and Number
Individual Date Folders Created Daily
Trigger folders created for all GPS trigger locations or manual markings
Individual Trigger folders
  PAR, BLF, MAT, MF4, AVI
The Data Center
CANape Data Date Folder
Trigger Folders
Individual Trigger Folder

## Slide 58
Eve Kit Software Installation
TSP-J-5014