## Slide 1
Eve Kit AZ Compatibility and Wifi Data Upload

## Slide 2
Eve Kit AZ Compatibility
Additional Hardware and Software Eve kit changes
Key Updates for Compatibility
Change Axis Quad IP Addresses
Run batch file to update Brick PC IP Addresses
Update Drive Letters and Rename
Add CAN21 to Vector Hardware for OxFord pluggin
Label CAN18/CAN21 spot on Eve Kit\
Update Vector Drivers to latest (25_10_0)
Update to CANape 21 SP 6 (Final upgrade for CANape 21)
Upgrades for Wifi Data Upload
Remove main USB slot, plug in and mount Wifi 6 Adapter
Update patch panel for one less USB (ensure no confusion or no empty ports)
Setup Synology Drive Client for wifi data upload to NAS
Andre

## Slide 3
Eve Kit Hardware Detail
Individual hardware components contained in the Eve kit
Main Eve Kit Components
VP7470 – Brick PC with 32 Gb RAM
VN1670 – 10 CAN, 5 LIN
VN5650 – 6 Ethernet, 2 CAN
VN1530 – 6 CAN
Axis F44 (x3) – Up to 4 Axis Cameras
ITS1_FD necessary for online tuning
VP7470 – Brick PC
VN1670
VN5650
F44 Axis Encoder

## Slide 4
Eve Kit Hardware Setup
Dedicated hardware CAN assignments for consistency and reliability
Same setup across ADT FH/SAC/AZ
Hardware Setup
Plug in specific CAN device to dedicated port on Eve Kit
  ITS1_FD -> CAN1, ITS2_FD -> CAN2, etc
Beneficial to ensure correct database files, recorded signals, and baud rates
Same hardware and patch panel layout across all 23 Eve Systems
  Exception, old axis cameras (no risk to new configurations)
Andre
CAN 1 - 16
CAN 17 - 18, LIN 1 - 2
ETH 1 - 3
Axis CAM5, CAM6

## Slide 5
Change Axis Quad IP Addresses
Same IP setup across ADT FH/SAC/AZ
Axis Quad IP Address Change
Manually change each Axis Quad IP Address in Axis software
  Axis Quad 1 -> 195.0.100.1
  Axis Quad 2 -> 195.0.100.2
  Axis Quad 3 -> 195.0.100.3
  Default Router = 195.0.100.10 (Same for all Axis)
Andre

## Slide 6
Change Brick PC Port IP Settings
Same IP setup across ADT FH/SAC/AZ
Brick PC Port IP Settings for Axis Cams
Place batch file in Brick Settings Folder
  This PC -> Downloads -> Brick Settings
  BrickPC_ip_config_New_Axis.bat
Confirm Network names are matching image on right
Right click batch file -> Run As Administrator
Assignments are the following, also shown below
  1G #1 -> 195.0.100.11
  1G #2 -> 195.0.100.12
  1G #3 -> 195.0.100.13
  1G #4 -> Same as Previous (192.168.4.1)
  10G #1 -> Same As Previous (192.168.10.10)
Andre
Batch File Placement
Required Network Naming

## Slide 7
Update Drive Letters and Rename
Same drive letter setup across ADT FH/SAC/AZ
Change Drive Letters
Previous D Drive -> Change to E Drive
  Rename to “Setup”
  This drive should have ~100Gb of space
Previous E Drive -> Change to D Drive
  Rename to “Data”
  Ensure this is the drive with 4+ TB of space
Andre

## Slide 8
Add to Vector Hardware
Add CAN21 for OxFord Setup
Open Vector Hardware Configuration
Right click CANape -> Application Channel Usage
Ensure all are 0 except the following:
  CAN = 22
  LIN = 5
  GNSS = 1
Andre

## Slide 9
Add CAN21 to Vector Hardware
Assign CAN18 and CAN21
Verify CAN and LIN
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN Channels are accurate
GNSS -> vGNSS Channel 1
Verify Vector Hardware looks exactly the same as image on the right
Andre

## Slide 10
Upgrade to latest drivers
For GPS as Vector Hardware Device
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN2 is VN1670 CH 5
Do not update Vector Platform Manager?
Andre
Confirm latest drivers work

## Slide 11
Upgrade to latest version of CANape 21
CANape 21 SP 6
Right click CAN18 -> choose VN5650 CH 14
Right click CAN19 -> choose Virtual CAN Bus 1
Right click CAN21 -> choose VN5650 CH 14
Ensure LIN2 is VN1670 CH 5
Do not update Vector Platform Manager?
Andre
Confirm latest CANape 21 version works

## Slide 12
Wifi Adapter Addition
Mount Wifi Adapter to Eve Kit
Plug into Brick PC
Mount Wifi Adapter to Eve Kit
Plug USB into Brick PC port 1
Remove patch panel slot for empty USB
  Shift HDMI port left 1
Andre
Need to put picture of official mounting location

## Slide 13
Wifi Data Upload Setup
Activate Wifi on Brick PC
Open file explorer
Choose CD drive Wifi 6 USB
Choose Driver Folder -> Setup.exe
Installation will begin!
  Wait to finish
  Will close automatically when complete
Andre

## Slide 14
Wifi Data Upload Setup
Connect to Orbi Router
After Wifi 6 installation is finished, window will close
Network connections will now have wifi option
Open wifi settings and find ORBI38 router
Choose connect automatically
Password = windylake010
Ensure connected successfully! (No internet, secured)
Andre

## Slide 15
Wifi Data Upload Setup
Install Synology Drive Client Software
Install Synology Client Software
  Software provided by Andre
Click through setup -> very simple
Andre

## Slide 16
Wifi Data Upload Setup
Setup Synology Drive Client
Open Synology Drive Client
Connect to NAS
  Synology NAS = 195.0.100.101, click search
  Choose ADT_DataCenter
  Username = ADT_EveUploader
  Password = PR0P!L0T
  Keep checked “Enable SSL”
  Click Next
Choose proceed anyway
Andre

## Slide 17
Wifi Data Upload Setup
Setup Synology Drive Client
Choose sync task -> click next
View original folder, edit paths on the next slide
Click change to edit folder to sync from NAS
Andre

## Slide 18
Wifi Data Upload Setup
Setup Synology Drive Client
Folder to sync from your NAS (195.0.100.101)
  Expand team folder
  Select CANape_Data
  Click OK
Folder location on your computer
  Expand D Drive
  Select only CANape_Data
  Uncheck create an empty “SynologyDrive” folder
  Click OK
Andre
Folder from NAS
Folder location on computer

## Slide 19
Wifi Data Upload Setup
Setup Synology Drive Client
Initial folder paths should look exactly like the image on the right
But wait not finished!
Click advanced
Under Folder
  Ensure CANape_Data is selected
  Every folder below should be auto selected, no need to change
Change to sync mode tab
Andre

## Slide 20
Wifi Data Upload Setup
Setup Synology Drive Client
Sync mode tab
  Check Upload data to Synology Drive Server Only
  Keep checked “locally deleted files”
  Keep checked “enable advanced consistency check
Ensure settings match the image on the right -> Click Apply!
Andre

## Slide 21
Wifi Data Upload Setup
Setup Synology Drive Client
Ensure file paths are still the same
Enable on demand sync checkbox will be removed automatically -> this is OK
Click done!
Andre

## Slide 22
Wifi Data Upload Setup
Setup Synology Drive Client
Click through everything (Next x4)
Ensure the sync task matches the settings on the right
  D:\CANape_Data
  One-way upload
Andre

## Slide 23
Wifi Data Upload Setup
See tasks when data starts to sync
Go to taskbar settings (right click on taskbar -> taskbar settings)
Scroll down -> Select which icons appear on the taskbar
Find Synology Drive Client -> Switch to ON
Andre

## Slide 24
Wifi Data Upload Setup
See tasks when data starts to sync
Go to D drive folder
Verify syncing status shows blue icon
  Syncing in progress
Green checkmark will show when that folder sync is complete
Andre
Sync in Progress
Sync Complete

## Slide 25
APPENDIX

## Slide 26
CANape Configuration - Setup
Setup page implemented from AZ configuration
Dedicated CAN assignments from hardware to match CANape software
New Setup page
Input Vehicle Project and Number
Select AD Mode -> Supports data driven tuning
Hardware Match
Check CAN boxes based on connected hardware
Selectable dropdown options for Ethernet channels based on Radar, Camera, and HD map type
Check Axis boxes based on external camera setup
Select commit to automatically enable/disable CANape networks in the Device Configuration
  Status of background network displayed with colored LED
  Axis camera views are live output
That’s it!
Andre

## Slide 27
CANape Configuration – Setup Online Tuning
Additional Steps for Online Tuning Configuration
Online Tuning Additional Setup
Navigate to Device Configuration
Expand Online_Tuning under CAN1
Select database -> Replace A2L file to online tune new vehicle
  Different A2L and PDX files for different vehicles
  Check page switching
Andre
Return to LKA1 Page
Ignition or engine on
Click online
Current LKA parameters will be retrieved from the ADAS module software

## Slide 28
CANape Configuration – Confirmation Drive
Take vehicle for data confirmation drive
Ensure green heartbeats and confirm active GPS triggers
Confirmation Drive
Start recording and drive test vehicle to M5 and back to office
  Test of active GPS triggers
  Test blue mode capable for AD2 vehicle
Ensure green heartbeats for successful signal recording
Ensure online tuning is working by verifying parameter changes are successful
Andre
External Comment Box
Executable built with C# to bypass CANape limitations
Allow for multiple comment boxes open at once
Ensures GPS triggers still successfully cut in the background
Turn comments on and off with convenient switch

## Slide 29
CANape Configuration – Automatic Data Cutting
Trigger 1 minute cutout files based on GPS location
New Trigger List Layout
GPS Trigger Output to Trigger List
Automatic cutting of data when driving through key scenes
Data comparing two runs at the same location can be overlaid and plotted easily
New trigger list structure for data review compatibility
New Trigger List
Free comment for individual trigger
GPS Trigger Scene Name
Trigger folder for individual run data

## Slide 30
CANape Configuration – Check Data
Output automatic data check report to confirm reliable data
Output Data Check Report
Return to office, stop recording, allow post processing
  Matlab conversion, automatic data transfer to SSD
Navigate to setup page, select Check Data box
  Check remaining E Drive space
  Script will automatically loop through each folder created from the various recorders
    Recorders 1, 2, 3 and Full
  Verify output file exists and is an appropriate file size (MF4, BLF, AVI, Trigger List CSV, KML)
  Check for important signals in individual MF4 files
    Yaw Rate, Steering Angle etc and ensure numerical output
  Confirm AXIS Camera videos files
  Confirm external SSD is recognized and fast copy is working
See result column to determine success or fail of individual tests
Andre

## Slide 31
CANape Configuration Setup - Additional
Full run MAT conversion to support data driven tuning
Continuous monitoring during driving to ensure no data errors
Full Run MAT Convert
Supports data driven tuning to make vehicle models
Automatic CANape function to convert additional data
Continue to add scripts and features that support users automatically for reliable data collection
  Avoid manual processing and sorting
Continuous Monitoring
Continuous checking of critical recording issues
  Example E drive space
  Pop up will show continuously until recording is stopped
Continue to add to this function to ensure no data loss during recording
Andre

## Slide 32
Data Organization
The Data Center Folder Structure Layout on SSD
CANape Data Organization Overview
The Data Center (CANape Data)
Automatic copy of CANape Data to SSD
Organization by Vehicle Project and Number
Individual Date Folders Created Daily
Trigger folders created for all GPS trigger locations or manual markings
Individual Trigger folders
  PAR, BLF, MAT, MF4, AVI
The Data Center
CANape Data Date Folder
Trigger Folders
Individual Trigger Folder